## Slide 1
. . . . . . . . . . . . . . . . . . . .
. . . . . . . . . . . . . . . . . . . .
bitbangers CPU
Devul, Sanjana, Aditya

## Slide 2: Overview of Design
. . . . . . . . . . . . . . .
. . . . . . . . . . . . . . . .
. . . . .
. . . .
RV32IMA_Zicsr_Zifencei (with some sv32 support).
5-stage pipelined in-order, static not-taken branch prediction, etc., etc.
CLINT (interrupt controller compatible w/privileged spec)
Behavioral UART for co-simulation.

## Slide 3: Datapath
. . . . . . . . . . . . . . .
. . . . . . . . . . . . . . . .
. . . . .
. . . .
IF/ID
Instruction Cache
PC
pc mux
+4
control_rom
ID/EX
rs1_idx
rs2_idx
regﬁle
immgen
EX/MEM
fwd_a
fwd_b
CMP
ALU
br_en
fwd_ctrl
MEM/WB
Data Cache
MBE
+4
LW
LB
LBU
LH
LHU
Hazard Detection Unit
EX
WB
MEM
MEM
WB
WB

## Slide 4: More on features
Atomics: LR/SC are implemented without reservation stations since it’s a uniprocessor.
AMOs (read-modify-write) are implemented by trapping and emulating using LR/SC.
Zicsr — diﬀicult extension to do correctly since lots of edge cases. Chose to stall for four cycles to ensure no hazards, since enforcing privileged spec’s read/write permission constraints plus hazards was very expensive in area and did not improve performance since CSR instructions are rare.
Zifenci — implementing simple write-update snooping-based cache coherence between I$ and D$ to prevent flushes of D$. (Bus contention is not a concern since I$ is never written to.) This way, D$ never has to write back every cacheline on fence.i, the instruction and data streams are always in sync via snooping.
. . . . . . . . . . . . . . . . . . . .
. . . . . . . . . . . . . . . . . . . .

## Slide 5: Why is nommu Nontrivial?
. . . . . . . . . . . . . . .
. . . . . . . . . . . . . . . .
. . . . .
. . . .
Requires building Linux in a certain way:
  uClibc instead of glibc, make sure the busybox initramfs is OK w/this.
  Create a flat binary instead of ELF so that we don’t need a bootloader/firmware.
  Requires writing a DTB (device tree blob) and loading into memory.
Testing this in simulation is…slow.
Booting even nommu Linux creates very large log files — our dump.fsdb
touches 3GiB+ on the previous boot.1
1EWS has a 10GiB/user ceiling that’s easy to hit :/

## Slide 6: What’s the Solution?
. . . . . . . . . . . . . . . . . . . .
. . . . . . . . . . . . . . . . . . . .
Write a cycle-accurate model of the processor, interrupt controller, other peripherals in C.
Boot Linux there, then use the software emulator as a specification for what the hardware should implement.
This allows us to have a golden model to compare instruction traces and processor state with.
Debugging the software emulator is much easier, since it’s about 400 lines of C (instead of ~3k lines of Verilog) and boots Linux in ~5 seconds.
Hardware/software co-design is a very useful tool, and likely the only way to actually do this project.

## Slide 7: Software emulator
. . . . . . . . . . . . . . .
. . . . . . . . . . . . . . . .
. . . . .
. . . .
We (very heavily) modified an RV32 emulator to be cycle-accurate with our processor.
Additional diﬀiculties: once interrupts are turned on, instruction traces can differ a lot due to emulator and simulated timers operating at different frequencies.
Needed to make the emulator cycle-accurate down to timing of interrupts between instructions.

## Slide 8: Writing a correct emulator that can boot Linux is hard!
. . . . . . . . . . . . . . .
. . . . . . . . . . . . . . . .
. . . . .
. . . .
Has involved building Linux many times in lots of different (experimental) ways.
Building the firmware (OpenSBI) with various configurations (RISC-V boot process is still a WIP and changes often).
Lots of reading Linux/OpenSBI source.
When comparing traces w/QEMU, finding abnormalities in how QEMU handles DTB — needed to read QEMU source and build QEMU with changes.
…and of course, reading the RISC-V specs.
Notes: fw_jump: jumps to fixed location. fw_payload: the firmware embeds the kernel. fw_dynamic: a previous stage tells opensbi where to jump to via a struct in memory

## Slide 9: Some results
. . . . . . . . . . . . . . .
. . . . . . . . . . . . . . . .
. . . . .
. . . .
Simulation ~1 million instructions takes 1 minute on VCS.
Emulator takes ~5 seconds to boot Linux (which is about 137 million instructions till the login program.)
Synthesis successful:
  Slack: 1.41
  Area: 18889.7237 ≈ 18900

## Slide 10: Edge cases!
. . . . . . . . . . . . . . . . . . . .
. . . . . . . . . . . . . . . . . . . .
Linux finds edge cases w/the processor very easily.
Correctness is extremely important.
Finding bugs is hard, since Linux assumes the underlying hardware is perfect, and fails silently — finding a failure in execution means comparing traces w/emulator.

## Slide 11: Examples of bugs
A load to precisely x2 followed by mret caused a hazard to be incorrectly detected, resulting in the mret never happening:
ld x2, (xX) mret
The symptom was an access to uninitialized memory — figuring out the issue was with return-from-trap required reworking the emulator’s timers till the traces matched exactly.
Interrupt flag was losing state: this was happening when an interrupt happened precisely after a multiplication operation — the stall in EX caused certain side effects.
An interrupt occurs at exactly the instruction used to turn interrupts off.
…so many more
. . . . . . . . . . . . . . . . . . . .
. . . . . . . . . . . . . . . . . . . .

## Slide 12: Currently working on
. . . . . . . . . . . . . . .
. . . . . . . . . . . . . . . .
. . . . .
. . . .
Further debugging nommu to boot.
Testing the new MMU/ sv32 in the emulator and booting MMU Linux in emulation.
  Caveat: flattening MMU Linux doesn’t seem possible, so we need to use firmware to boot an ELF Linux — currently exploring OpenSBI’s fw_payload and comparing emulator traces w/QEMU.
Finishing sv32 in hardware and (finally) booting Linux there.

## Slide 13: What we should’ve done differently
. . . . . . . . . . . . . . . . . . . .
. . . . . . . . . . . . . . . . . . . .
Started earlier — this project is probably a 2.5 month project, not a 1 month one.
Tried booting a smaller, simpler RISC-V operating system — unfortunately these are rare.
Started FPGA prototyping earlier — waiting for Linux to boot in simulation makes TDD very slow.

## Slide 14
. . . . . . . . . . . . . . . . . . . .
. . . . . . . . . . . . . . . . . . . .
Booting nommu Linux…to some point.

## Slide 15
. . . . . . . . . . . . . . . . . . . .
. . . . . . . . . . . . . . . . . . . .
Q/A